## Slide 1: AVC/H.264 HRD Easy Overview
Composed by Shevach Riabtsev
riabtsev@yahoo.com

## Slide 2: General Flowchart
TS (MB) Buffer
CPB
DPB
Instantaneous
Decoder
AVC/H.264 spec.
BitRate
Signaled
removal
Signaled Removal
ES
ES
Reconstr.
picture
Signaled Removal

## Slide 3: Details
CBP Size (in bits) is specified in VUI via cpb_size_value_minus1 and cpb_size_scale as
CpbSize = ( cpb_size_value_minus1+ 1 ) <<(4+ cpb_size_scale)
The bitrate (bits per second) is specified in VUI via bit_rate_value_minus1 and bit_rate_scale as
BitRate = (bit_rate_value_minus1+1)<<(bit_rate_scale+6)
DPB Size granularity is in units of frames and specified in VUI by
max_dec_frame_buffering, if this parameter not present derived from Table A-1 of the spec. according to level
Removal Time from DPB is specified in picture timing SEI by
dpb_output_delay, this parameter is signaled for each picture. Frame is removed from DPB instantaneously.
Removal Time from CPB is specified in picture timing SEI by
cpb_removal_delay, this parameter is signaled for each picture. Frame is removed from CPB instantaneously.
Note:
Frames are removed from CPB instantaneously and immediately decoded instantaneously and put onto DPB instantaneously. In other words a frame moves from CPB to DPB in 0 seconds.
Therefore HRD model is called Hypothetical.

## Slide 4: Details and Notes
TS buffer is not specified in H.264/AVC. However, it’s specified in Blu-Ray spec. (named as MB1 or Multiplexor buffer) and it has a constant size of 40000 bytes (Table 8-3 of Blu-Ray spec).
The input rate to TS buffer is leak rate (the rate is specified in Table 8-2 of Blu-Ray spec). For level 4.1 the input rate is 1.2*40*10^6 bits/sec.
cpb_removal_delay denotes the frame removal time (in units of clock ticks, details are present in the next slide) from the last buffering period SEI.
Thus, cpb_removal_delay is monotonically increasing along frames until next buffering_period SEI message encountered. The number of bits allocated for cpb_removal_delay is specified by the VUI parameter cpb_removal_delay_length.
One should choice the magnitude of cpb_removal_delay_length such that no wrap-around occur within the maximal buffering-period interval.
  For example, if we specify cpb_removal_delay_length=8 bits and the frame duration is 2 clock ticks, but the number of frames between two buffering period SEIs is greater than 512 then we can’t keep cpb_removal_delay monotonically increasing.

## Slide 5: When Frames Removed from CPB?
Frame is removed from CPB according to cpb_removal_delay (signaled in the pic_timing SEI associated with the given frame).
cpb_removal_delay is specified in units of clock ticks from arrival of the last buffering_period SEI
Clock Tick (Tc) is derived from num_units_in_tick and time_scale (signaled in VUI) as
Tc = num_units_in_tick /time_scale
Tc also specifies the duration of field in seconds, hence the duration of frame is 2 x Tc seconds.
To convert cpb_removal_delay to seconds use the following:
cpb_removal_delay * Tc
The removal time Tr( n ) of the frame #n from CPB is specified as follows:
Tr( n ) = Tr( last buffering period ) + tc * cpb_removal_delay( n )
Usually the buffering period SEI is signaled at the start of GOP (not necessarily each GOP)

## Slide 6: When Remove Very First Frame from CPB?
The initial removal time ( or removal time of the very first frame) in seconds is specified by initial_cpb_removal_delay/90000, where initial_cpb_removal_delay is signaled in buffering_period SEI.

## Slide 7: When Data starts to Flow to TS buffer and Restrictions ?
The start time (Big Bang) is specified by the first PCR arrived, from that event data flows to TS buffer and is “drained” to CPB with the predefined rate BitRate (remind TS-buffer is leaky).
Only after initial_cpb_removal_delay/90000 seconds Decoder starts to work, i.e. to remove data from CPB. Thus, the decoding delay is equal to initial_cpb_removal_delay/90000 .
Blue-Ray standard limits the maximal decoding delay to 1 sec., i.e. initial_cpb_removal_delay < 90000. The maximum delay of 1 second puts some restrictions on CPB size and BitRate. If we divide a declared CPB buffer size (CpbSize) with a declared bit-rate (BitRate) then the result must be less or equal to 1, if not, either the buffer size should be reduced or BitRate should be increased.

## Slide 8: More Relevant Definitions
Ta(n) - the time when the first bit of the picture #n enters the CPB, called the arrival time of picture #n.
Tf(n) - the time when the last bit of the picture #n enters the CPB, called the final arrival time of the picture #n. Tf(n) is equal to Ta(n)+PictureSize/BitRate.
Tr(n) – the time when the picture #n is removed from the CPB, called the removal time.

## Slide 9: VBR and CBR Modes
CBR – signaled by cbr_flag=1 in VUI.
In this mode data from TS buffer flows with a constant predefined rate BitRate, i.e. the tap between TS and CPB is always open and never closed even for a moment. In CBR mode Ta(n) = Tf(n-1).
VBR - signaled by cbr_flag=0 in VUI.
In this mode the tap between TS and CPB can be closed temporarily (to prevent CPB overflows), however when the tap is open data flows with constant rate BitRate. Hence, Ta(n) ≥ Tf(n-1).
Note: in both modes the bit-rate to CPB is specified as
BitRate = (bit_rate_value_minus1+1)<<(bit_rate_scale+6)
Where bit_rate_value_minus1 and bit_rate_scale are signaled in VUI.

## Slide 10: CBR Mode Example
The figure is taken from JVT-D131 “HRD and Related Issues” by Eric Viscito

## Slide 11: VBR Mode Example
The figure is taken from JVT-D131 “HRD and Related Issues” by Eric Viscito

## Slide 12: How Arrival Time Derived in VBR mode?
Unlike CBR mode, Ta(n) > Tf(n-1). In other words in the period of [Ta(n) – Tf(n-1)] seconds the tap is closed.
Before let’s specify what is Te(n) – earliest time for the picture #n to enter:
a) For non-IDR frame
Te(n) = Tc*cpb_removal_delay(n) + Tr(last idr) –(initial_cpb_removal_delay+initial_cpb_removal_delay_offset)/90000
where Tc = num_units_in_tick /time_scale
b) For IDR frame
Te(n) = Tc*cpb_removal_delay(n) + Tr(last idr) – initial_cpb_removal_delay/90000
The arrival time of frame #n is
Ta( n ) = Max( Tf( n − 1 ), Te( n ) )